## Slide 1: The Floor
Cut away the flat side channel & replace with true 3D channel: (Evergreen .100”)
Cut out the original floor from nearly bolster to bolster & replace with a new floor.
New floor made from Evergreen sheet flush with the bottom of the old floor depth.
Cut and fit the replacement floor with great care!
New Center sill channel made from Evergreen 5/16” channel remove wedges
from the ends of the web to get the tapered look, but don’t cut away the flanges.
New floor and details added
APWS water tank
S/E Valve box (2)
Battery boxes
UC Brake Set
Vapor traps (2)
Battery charging receptacles (2)

## Slide 2: Diner details Aisle side, kitchen end
Diaphragm
Air, steam & signal lines
Cut levers
Body mounted KD’s
Marker light brackets
Grab irons
Kitchen door
Stirrup steps
Window sills
Gutters, scale 1” x 2” strip
preformed & glued on edge
Ice hatch
Square Kitchen vents (2)
Round hooded & wind vanned Kitchen vents (2)
SE A/C hatches (2)
Enlarged End Sills

## Slide 3: Flat Kit Side Scrabble
The diner. Build & detail the roof kitchen end, kitchen side.
‘Mushroom” vent 1/16”rod + tube
Roof rivet strips 0.005”
Gutters, scale 1” x 2” strip
preformed & glued on edge
A/C ducts: NERS parts
Grab irons
(various locations)
“wind vane” vent: 1/8” tube, formed aluminum cap, 0.010” vane
Box vent: 0.010” base flange, 0.030” body, angle & sheet top
“Ice hatch” 0.020” sides , 0.010” lid, 0.005” hinge leaf & 0.010 rod hinge , brass wire handle,
Lid stop brace: brass shim
The roof is a model within a model, especially so for diners with A/C.
Pantry area ice hatch: 0.010” base flange , 0.030” body, 0.010” lid, 0.005” hinge leaf & 0.010 rod hinge , brass wire handle,
Vent frames (6)
Service platform: Shim brass support legs, 2” x 3” strip for decking

## Slide 4: Roof Top S/E A/C hatch detailing
Long grab iron with ladder notches
(various locations)
Gutters, scale 1” x 2” strip
preformed & glued on edge
The café lounge shown, same components on the diner, but split locations
‘Mushroom” vent 1/16”I.D. rod + tube
Hatch base: 0.030” sheet, creased & bent for “peak”
Hatch cover: 0.010” sheet, creased & bent for “peak”, W/ rivet detail
Hatch cover hold down dogs: 0.010” X 0.015” flat brass bar
Roof vent , round tube trimmed & capped

## Slide 5: Truck Modifications
Moveable support bars
Pulley
Generator
Belt tensioner
Belt
Generator support bar (truck mounted part)